## Slide 1: CFJ-A6421 – New case setup
Aerodynamics & CFD Lab
University of Miami

## Slide 2: Steps to generate organized Large mesh
0 From the geometry, find the right mesh topology
1 Generate big blocks
  Big blocks 1 for outer mesh
  Big blocks 2 for inner mesh
2 use blocksplitter.o to split to small blocks
3 Import the splitted blocks to pointwise
4 check the volume and skewness
5 Export the whole mesh
Big blocks 1
Big block 2

## Slide 3: Multi-Block distribution
Block 1-300
Outer mesh 1-300
Inner mesh 301-348
INJ Block 301-304
Connect 305-344
SUC Block 345-348
Block 301-348

## Slide 4: BC setup
Inlet bctype = 6: eta=60, block 201-249(49)
Outlet bctype = 5: eta=60, block 250-300(51)
CFJ Inj bctype = 9: xie = 1, block 301-304(4)
CFJ Suc bctype = 5: xie=10, block 345-348(4)
Periodic bctype = 10
                zta=1, block 1-348(348)
                zta=50, block 1-348(348)

## Slide 5: Edit the bcdefine.datain.small
Inlet bctype = 6: 49 blocks, eta=60, 201-249
Outlet bctype = 5: 51 blocks, eta=60, 250-300
CFJ Inj bctype = 9: 4 blocks xie = 1, 301-304
CFJ Suc bctype = 5: 4 blocks xie=10, 345-348
Periodic bctype = 10: 348 blocks zta=1, 1-348
Periodic bctype = 10: 348 blocks zta=50, 1-348
6,49 ! bctype, number of blocks, Inlet
201,2,60 ! start block, bc-dir(1,2,3), bc_minmax(1,max)
5,51 ! bctype, number, Outlet
250,2,60 ! start block, bc-dir(1,2,3), bc_minmax(1,max)
10, 348 ! bctype, number, Periodic
1,3,1 ! start block, bc-dir(1,2,3), bc_minmax(1,max)
10, 348 ! bctype, number, Periodic
1,3,50 ! start block, bc-dir(1,2,3), bc_minmax(1,max)
9,1 ! bctype, number, Injection inlet
301,1,1 ! start block, bc-dir(1,2,3), bc_minmax(1,max)
5,1 ! bctype, number, Suction outlet
348,1,20 ! start block, bc-dir(1,2,3), bc_minmax(1,max)
-1, 0 !last line
The BC definition for each groups are represented by two consecutive lines
eg, the first two lines represent the inlet blocks definition,
6,49 ! bctype, number of blocks, Inlet
201,2,60 ! start block, bc-dir(1,2,3), bc_minmax(1,max)
The file ends with -1, 0

## Slide 6: Edit & Run the NewCaseSetup1.sh Automatic
4 steps
1 processing.out
  bin_3d_001.dat …
  init.input
2 Pre_bc7
  Find all the bc7
  pre_bc7_datain, pre_bc7.err
3 Sort out other BCs
  bcdefine.datain
  bcoutput7.datain
  bcoutputbc.datain
  bcoutputwall.datain
  datain.bc
4 export to output folder
  Inside the folder: bin, datain.bc,init.input
#! /bin/bash
#1. --> init.input, bin*.dat
echo "~~~~~~~~~~~~~~~FASIP Newcase BC setup~~~~~~~~~~~~~~~~"
echo "~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~"
echo "Attention: make sure bcdefine.datain.small is correctly defined"
echo "Step 1 generate bin file and init.input"
./processing.out <<EOF
1
LES-grid-348-206050.x
3
1
62.0
0.25
0
EOF
echo "Step 1 finished"
echo "Step 2 find bc7"
./pre_bc7_2d3d.o <<EOF
1d-8
3
EOF
echo "Step 2 finished, check the pre_bc7.err file "
echo "Step 3 sort datain.bc"
python Sort-Combine_datain_output.py
echo "Step 3 finished"
#4 export to output
if [ ! -d output ]; then
mkdir output
fi
mv bin* datain.bc init.input output
NewCaseSetup1.sh

## Slide 7: Run the previous steps manually
./processing.out
./pre_bc7_2d3d.o
python Sort-Combine_datain_output.py

## Slide 8: Things to remember
1 Before run the code, check the files are complete
  bcdefine.datain.small
  Grid file
  NewCaseSetup1.sh (check the grid name, AoA and references)
  pre_bc7_2d3d.f
  pre_bc7_2d3d.o
  PrebcAll.f
  PrebcAll.o
  processing.out
  Processing.sh
  Sort-Combine_datain_output.py
2 After run the code, remember to doublecheck the init.input and datain.bc
  Init.input: special BC setup for CFJ
  Datain.bc: check the correct BC definition